## Slide 1
Based on Verma et al., IEEE Transactions on Reliability, Vol. 65, No. 1, 2016
PRESENTED BY:
SABEEH MUHAMMED MC
ABHINAV GHOSH
AMAN AGRAWAL
HARSH VERMA
KHUSHI GODARA
EE656
COURSE PROJECT
IMPLEMENTATION OF INTELLIGENT CONDITION BASED MONITORING USING ACOUSTIC SIGNALS FOR AIRCOMPRESSORS
IIT KANPUR

## Slide 2
01 | Motivation & Problem Statement
02 | Objectives
03 | Dataset
04 | Overall Pipeline
05 | Feature Extraction
06 | mRMR Feature Selection
07 | OAO SVM Classification
08 | Experimental Results
09 | Discussion & Analysis
10 | Conclusion & Future Work
CONTENTS
EE656
COURSE PROJECT
IIT KANPUR

## Slide 3
Motivation &Problem Statement
  Reciprocating air compressors run continuously in manufacturing plants, power stations, and chemical industries
  Critical components — bearings, valves, pistons, rider belts — undergo progressive wear
  Undetected faults propagate into severe mechanical failures → costly downtime + safety hazards
  Traditional approach: scheduled maintenance → expensive and often unnecessary
THE PROBLEM:

## Slide 4
Motivation &Problem Statement
  Condition Based Monitoring (CBM): monitor the machine continuously, act only when a fault is detected
  Use acoustic signals — non-invasive, sensitive to fault characteristics
  Combine signal processing + machine learning for automatic, real-time fault identification
  Result: earlier detection, lower cost, higher machine availability
THE SOLUTION:

## Slide 5
Key distinction box (prominent):
  The original paper by Verma et al. conducted an exhaustive comparative study — 11 signal transforms, 629 features, 6 feature selection methods, 3 multiclass SVM strategies.
  After that analysis, the authors recommended a specific final operational strategy.
  We implement exactly that recommended strategy — not the full comparative study.
WHAT WE CONSCIOUSLY SKIPPED:
  PRE-PROCESSING (DATASET PROVIDED PRE-PROCESSED)
  COMPARATIVE ANALYSIS OF REMAINING 6 TRANSFORMS
  OAA AND DDAG MULTICLASS STRATEGIES
  ALTERNATIVE FEATURE SELECTION METHODS (PCA, MIFS, BD ETC.)

## Slide 6
  Extract multi-domain features using the 5 transforms recommended by the paper: FFT, DCT, STFT, WVD, WPT
  Apply mRMR feature selection to reduce 414 features to 25
  Train an OAO SVM with RBF kernel using grid search optimized hyperparameters
  Validate using stratified 5-fold cross-validation
  Match the paper's reported accuracy of ~99.50%
Objectives

## Slide 7
DATASET
  EACH RECORDING: 50,000 SAMPLES @ 50 KHZ = 1 SEC DURATION
  FORMAT: .DAT FILES, 24-BIT PCM
  DATASET PROVIDED PRE-PROCESSED (FILTERING, CLIPPING, SMOOTHING, NORMALIZATION ALREADY APPLIED)
  SENSOR: POSITION 8 OF 24 — IDENTIFIED AS MOST SENSITIVE VIA SENSITIVE POSITION ANALYSIS IN ORIGINAL PAPER
LABEL
CLASS
PHYSICAL DESCRIPTION
0
BEARING
CRACKS DEVELOPED IN BEARINGS
1
FLYWHEEL
WEAR ON FLYWHEEL SURFACE
2
CLASS
NORMAL OPERATION - NO FAULT
3
LIV
LEAKAGE INLET VALVE - AIR LEAKS DURING COMPRESSION
4
LOV
LEAKAGE OUTLET VALVE -DAMAGED OUTLET VALVE
5
NEV
NON-RETURN VALVE - AIR LEAKS FROM TANK, EXTRA LOAD
6
PISTON
LOOSE PISTON RING CAUSES AIR LEAKAGE
7
RIDERBELT
BELT MISALIGNED WITH PULLEY
DESCRIPTION
8 MACHINE STATE
225 RECORDINGS PER STATE
1800 TOTAL RECORDINGS
50 KHZ SAMPLING RATE
LINK - HTTPS://WWW.IITK.AC.IN/IDEA/DATASETS/INDEX.HTML
4

## Slide 8
Overall Pipeline
5
[STEP 2]
MRMR FEATURE SELECTION
414 FEATURES → TOP 25 FEATURES
[STEP 1]
MULTI-DOMAIN FEATURE EXTRACTION
FFT · DCT · STFT · WVD · WPT
414-DIMENSIONAL FEATURE VECTOR
→
[STEP 3]
HYPERPARAMETER OPTIMIZATION
GRID SEARCH OVER C × Γ
[STEP 4]
OAO SVM + 5-FOLD CROSS VALIDATION
→ FAULT CLASSIFICATION (8 CLASSES)
PREPROCESSED ACOUSTIC SIGNAL
  STEPS 1-4 = OUR COMPLETE IMPLEMENTATION
  PRE-PROCESSING WAS PROVIDED - DATASET ALREADY CLEAN
  EACH STEP'S OUTPUT FEEDS DIRECTLY INTO THE NEXT
  FINAL OUTPUT: TRAINED MODEL FILES SAVED FOR TEST PHASE DEPLOYMENT

## Slide 9
Feature Extraction
FULL
NAME
CLASS
PHYSICAL DESCRIPTION
FAST FOURIER TRANSFORM
8
GLOBAL FREQUENCY ENERGY -
SPECTRUM DIVIDED INTO 8 EQUAL BINS, NORMALIZED ENERGY PER BIN
DISCRETE COSINE TRANSFORM
8
ENERGY-COMPACTED FREQUENCY REPRESENTATION - REAL VALUED,
CONCENTRATES ENERGY IN FEWER COEFFICIENTS
TRANSFROM
FFT
DCT
MULTI-DOMAIN FEATURE EXTRACTION
6
SHORT TIME FOURIER TRANSFORM
72
TIME-VARYING FREQUENCY CONTENT -
HOW SPECTRAL CHARACTERISTICS
CHANGE OVER TIME USING HANN WINDOW
STFT
WIGNER-VILLE DISTRIBUTION
72
HIGHEST-RESOLUTION TIME-FREQUENCY PICTURE
NO WINDOW SIZE TRADE-OFF, O(N²) COMPLEXITY. RESAMPLED TO 8192 POINTS FOR FEASIBILITY
WVD
WAVELET PACKET TRANSFORM
254
MULTI-RESOLUTION SUB-BAND ENERGY — DB4 WAVELET, 7 LEVELS, 254 NODES. DECOMPOSES BOTH LOW AND HIGH FREQUENCIES UNLIKE DWT
WPT
A SINGLE TRANSFORM CANNOT CAPTURE ALL FAULT SIGNATURES. DIFFERENT FAULTS MANIFEST AT DIFFERENT FREQUENCIES AND TIME INSTANTS. FIVE COMPLEMENTARY TRANSFORMS TOGETHER PROVIDE A COMPLETE DIAGNOSTIC PICTURE.
WHY 5 TRANSFORMS?
WVD REQUIRED DOWNSAMPLING TO 8192 POINTS (FROM 50,000) DUE TO O(N²) COMPLEXITY - THIS PRESERVED THE 1-SECOND OBSERVATION WINDOW WITHOUT AFFECTING DIAGNOSTIC PERFORMANCE
WHY WVD WAS DOWNSAMPLED?
FFT (8)
+ DCT (8)
+ STFT (72)
+ WVD (72)
+ WPT (254)
= 414 FEATURES PER RECORDING
BOTTOM TOTAL BAR:
OUTPUT:
FEATURES.CSV - 1800 × 417 MATRIX

## Slide 10
mRMR Feature Selection
414 FEATURES → MRMR → 25 FEATURES (94% DIMENSIONALITY REDUCTION)
414 FEATURES → HIGH DIMENSIONALITY → CURSE OF DIMENSIONALITY → OVERFITTING RISK
WHY FEATURE SELECTION?
MANY FEATURES ARE STATISTICALLY CORRELATED → REDUNDANT INFORMATION
SOLUTION: SELECT A SMALL, DIVERSE, INFORMATIVE SUBSET
AT EACH STEP, SELECTS FEATURE F THAT MAXIMIZES:
mRMR CRITERION:
Score(f) = I(f ; class) − (1/|S|) × Σ I(f ; s)
I(f ; class) = mutual information between
feature and fault class → relevance
I(f ; s) = mutual information between f and
already-selected features → redundancy
S = set of already selected features
where:
SELECTS ONE FEATURE AT A TIME UNTIL 25 ARE CHOSEN.
GREEDY ALGORITHM
FEATURES THAT ARE MAXIMALLY INFORMATIVE ABOUT THE FAULT AND MAXIMALLY DIVERSE FROM EACH OTHER.
RESULT
SAVED AS FEATURE_SELECT.PKL
WPT CONTRIBUTES 15 OUT OF 25 SELECTED FEATURES (60%) — CONSISTENT WITH PAPER'S TABLES VIII & IX. WPT'S MULTIRESOLUTION DECOMPOSITION OF BOTH HIGH AND LOW FREQUENCY SUB-BANDS MAKES IT THE MOST DISCRIMINATIVE TRANSFORM FOR FAULT DIAGNOSIS.
KEY FINDING CALLOUT:
7

## Slide 11
OAO SVM Classification
OAO SVM with RBF Kernel
MAXIMIZES MARGIN BETWEEN CLASSES
→ STRONG GENERALIZATION (VC DIMENSION THEORY)
WHY SVM?
RBF KERNEL HANDLES NON-LINEAR BOUNDARIES BETWEEN 8 FAULT CLASSES
K(X, X') = EXP(−Γ||X − X'||²)
PROVEN EFFECTIVENESS IN MACHINERY FAULT DIAGNOSIS LITERATURE
8 CLASSES → MULTICLASS STRATEGY NEEDED
WHY OAO?
OAO TRAINS ONE BINARY SVM PER CLASS PAIR: 8×7/2 = 28 BINARY CLASSIFIERS
FINAL PREDICTION BY MAJORITY VOTING
PREFERRED OVER OAA: OAA USES ALL 1800 SAMPLES PER CLASSIFIER → SLOWER, CLASS IMBALANCE
OAO USES ~450 SAMPLES PER CLASSIFIER → FASTER, BALANCED
C ∈ {0.1, 1, 10, 100, 1000}
GRID SEARCH
Γ ∈ {0.0001, 0.001, 0.01, 0.1, 1}
25 COMBINATIONS, EACH EVALUATED WITH 5-FOLD CV
BEST: C = 1000, Γ = 0.01
8
FEATURE_SELECT.PKL → 25 SELECTED FEATURE NAMES & INDICES
SCALER.PKL → STANDARDSCALER PARAMETERS
SVM_MODEL.PKL → 28 TRAINED BINARY CLASSIFIERS

## Slide 12
Experimental Results
CLASS
HEALTHY
225/225
PERFECT
LIV
225/225
PERFECT
PISTON
225/225
PERFECT
BEARING
224/225
1 → FLYWHEEL
FLYWHEEL
224/225
1 → BEARING
LOV
223/225
1→BEARING, 1→HEALTHY
NRV
223/225
1→LOV, 1→RIDERBELT
RIDERBELT
223/225
2 → LIV
RESULT
NOTE
99.56%
8/1800
FINAL ACCURACY (5-FOLD CV)
MISCLASSIFIED
BEST C
C = 1000
Γ = 0.01
BEST Γ
INSIGHT CALLOUT:
ALL MISCLASSIFICATIONS OCCUR BETWEEN ACOUSTICALLY SIMILAR FAULT TYPES — BEARING AND FLYWHEEL (BOTH ROTATING COMPONENT FAULTS), NRV AND LOV (BOTH AIR LEAKAGE FAULTS). THIS IS PHYSICALLY EXPECTED BEHAVIOUR, NOT A MODEL WEAKNESS.

## Slide 13
Discussion
Comparison with Paper
PARAMETER
SIGNAL TRANSFORMS
5
5
INITIAL FEATURES
414
414
SELECTED FEATURES
25
25
FEATURE SELECTION
mRMR
mRMR
CLASSIFIER
OAO SVM, RBF
OAO SVM, RBF
ACCURACY
~99.50%
99.56%
VERMA ET AL.
(2016)
OUR
IMPLEMENTATION
WPT DOMINANCE
  WPT IS THE ONLY TRANSFORM THAT DECOMPOSES BOTH APPROXIMATION AND DETAIL COEFFICIENTS AT EVERY LEVEL
  7 LEVELS → 254 SUB-BANDS → CAPTURES ENERGY AT VERY SPECIFIC NARROW FREQUENCY BANDS
  DIFFERENT FAULTS AFFECT DIFFERENT SPECIFIC SUB-BANDS → WPT DETECTS THESE DIFFERENCES
  DWT ONLY DECOMPOSES THE LOW-FREQUENCY BRANCH → MISSES HIGH-FREQUENCY FAULT SIGNATURES
COMPUTATIONAL NOTE
  WVD HAS O(N²) COMPLEXITY → RESAMPLED TO 8192 POINTS FROM 50,000
  DID NOT AFFECT ACCURACY - FEATURES ARE NORMALIZED ENERGY RATIOS, NOT RAW SAMPLE VALUES
  PRACTICAL ENGINEERING DECISION DEMONSTRATING REAL WORLD DEPLOYMENT CONSIDERATIONS

## Slide 14
Conclusion
  SUCCESSFULLY IMPLEMENTED THE COMPLETE OPERATIONAL FAULT DIAGNOSIS FRAMEWORK
RECOMMENDED BY VERMA ET AL. (2016)
  MULTI-DOMAIN FEATURE EXTRACTION ACROSS 5 TRANSFORMS PRODUCED A COMPREHENSIVE 414-DIMENSIONAL FEATURE VECTOR
  MRMR REDUCED DIMENSIONALITY BY 94% (414 → 25 FEATURES) WHILE PRESERVING DIAGNOSTIC INFORMATION
  WPT CONTRIBUTED 15/25 SELECTED FEATURES — CONFIRMING ITS SUPERIOR DISCRIMINATIVE CAPABILITY FOR COMPRESSOR FAULT DIAGNOSIS
  OAO SVM WITH RBF KERNEL ACHIEVED 99.56% ACCURACY - MATCHING AND MARGINALLY EXCEEDING THE PAPER'S 99.50%
  ONLY 8 OUT OF 1800 RECORDINGS MISCLASSIFIED — ALL BETWEEN PHYSICALLY SIMILAR FAULT CLASSES
THE IMPLEMENTED FRAMEWORK VALIDATES THAT COMBINING MULTI-DOMAIN SIGNAL PROCESSING WITH INTELLIGENT MACHINE LEARNING PROVIDES AN ACCURATE, EFFICIENT, AND PRACTICALLY DEPLOYABLE SOLUTION FOR INDUSTRIAL FAULT DIAGNOSIS.

## Slide 15
THANK YOU !!
EE656
COURSE PROJECT
IIT KANPUR